## Slide 1: D’17O data reduction code
5/5/2021

## Slide 2: Overview of code
Format the lab data file (ReactorSpreadsheetFormatter)
  Reactors 6 and before use a different spreadsheet setup
Correct the data (IPL_17O_correction)
  Tests for appropriate priming
  Finds analyst-specified segments within a Reactor
  Basic SMOW-SLAP
  Linear SMOW-SLAP
  Segmented SMOW-SLAP (includes Basic and Linear corrections for each segment)
  Corrects D’17O of carbonates based on 102-GC-AZ01, or user setting (could be extended to phosphates in the future)
  Corrects d’18O of carbonates based on d18O(CO2/CaCO3) analyses (standards and any analyzed samples)
  Corrects d’17O of carbonates based on revised D’17O and d’18O values (assumes lambda = 0.528)
  Makes summary tables and plots
  Sets up a post-processing matrix that forces user input to select the appropriate normalization scheme
Make lists of all corrected data and their averages (IPL_17O_Sorting)
  Makes final data lists based on user-selected normalization scheme for each Reactor Segment (Basic, Linear, Segmented-Basic, Segmented-Linear)